Configuring Static Recording on

X91, X91+, X900, X900+ and X91

GPS Receivers

By:	Mark Silver

Date:	2013 September

NOTE: if you have a ‘Plus’ receiver (X91+ or X900+) then the file transfer tools in HcLoader won’t work; but the settings tool will be just fine. Use the USB plug to mount the receiver as a thumb-drive and gain access to your files.

- Download the HcLoader.exe tool to your machine. NOTE: This tool may not work on 64-bit OS’s.

- Connect serial port to receiver. Use USB to Serial convertor if your computer does not have a built in serial port (few do.)

- Start the tool

Chinese

If you start the HCLoader.exe program and you see Mandarin Chinese characters, and that is a problem:

you can switch to English by clicking on the menu option ‘L’ and then ‘E’.

Then exit the program and restart for English titles and menus.

- Click on the ‘Setup’ button.

- Verify that the serial number matches the receiver you have connected.

- You can set the 
‘Sample Interval’		Rate to store points, 1 – 5 – 15 are standard settings
‘Mask Angle’			Track SV’s above set angle
‘Data Log’			Auto will start logging when receiver is turned on
‘Data Logging, Sessions’	Automatically closes file after set period
‘Port Configuration’		Choose ‘Normal Mode
‘Work Mode’			Default “No Auto Base”
‘Correction Port’		if auto base, then this is where the corrections go to
‘Format of Correction’	RTCM2, RTCM3, CMR+, CMR

- Click on ‘Apply’ after making changes to save new settings to the head.

- ‘Update’ reads the settings from the head.