N71| Applications

Ntrip Reference Station

The workflow of Set N71 as Reference station

N71 can perform as a Internet Ntrip Reference Station.

Preparations: Apply the static IP from your internet provider; open the TCP and HTTP protocol for some Ports.

Also you need some construction to fix the antenna, after this you have to using static survey to calculation the coordinates

## 1. Installation N71 receiver

Connect N71 with PC using data +power cable like the figure. And Power on.

## 2. Setting static IP by winflash.

Run Winflash on PC. And follow the steps below.

The latest version of Winflash can be found in Trimble Website: http://www.trimble.com/gpsinfra_ts.asp?Nav=Collection-70648.

For example: we apply static IP: 222.44.183.12 from the network provider, and we do the port hard set on the Router 192.168.0.132(local area network IP), for this IP we set 9906 port as TCP service (NTRIP caster port), so the NTRIP server IP: 222.44.183.12:9906; 9908 is for HTTP service (Remote control), we can using the http://222.44.183.12:9908 to log on N71 to do remote control.

## 3. Set N71 as a Ntrip Reference Station on the Website

Log on the IP address and particular port in IE Brower like the format: HTTP://222.44.183.12:9908,  Key in user name: admin and password: password to log in as an administrator.

## 3.1.  Set Base information

3.2. Set Ntrip Information

## 4. Create Users and their authority

This is the function to define the user name, password and their authority to log in this new N71 CORS.

CHC - Shanghai HuaCE Navigation Technology Ltd.

Building 35, n° 680Guiping Road

200233	Shanghai – China

Last review by Simon: 23th Oct 2012

Tel :	+86 21 542 60273

Fax:	+86 21 649 50 963

Email : sales@chcnav.com	|	www.chcnav.com

# Text boxes

N71 set as Reference station

Installation N71, Fix antenna, calculation coordinates of antenna

Apply Static IP from Internet Provider

Configuration IP of N71 to static IP

Set NTRIP caster

Set Reference station coordinates

NTRIP end user, X900, X91, LT400, GPS receiver log on server gets correction data

Register user name and password for end user

Data+PowerCable

GNSS Antenna Cable

Figure of N71 Cable Connection

Configure ethernel settings

Choose the right COM Port

Processing

Finish

Choose Static IP address in IP Setup option, fill the following IP information and Port

When 100% was shown, Exit

Website Main Interface

In Receiver Configuration —Reference Station: Input Known position , key in the Reference station coordinates, or click here to read the current position(unknown coordinates )

Click OK to accept the setting

In I/O Configuration — Port Summary: Click one of the NTRIP Caster name.

Enable this port first by tick the box of Enable and distribute a valid port for Ntrip visit. Add some station information like Country or description. Most important is to give a Mount Point Name which will shows as a source list when Ntrip client log in. Also you need activate a correction message type like CMR or RTCM by choosing the corresponding name in the following drop-down list box.

Click OK to confirm the setting

When this IP and port was used by client, the background will turn green.

In Port Summary, check the selected message type has successfully set in the certain port

In Security—Configuration—define the username password and the authority by tick the relative box, if only used to log in CORS, NTripCaster will be enough

The existing Account and Authority can be seen at Security--Summary